High speed Automatic Flute Laminator

- Machine:

- Specifications:

| Model | ―1300 | ―1450 | ―1650 |
| --- | --- | --- | --- |
| Max. Sheet Size | 1300mmx1000mm | 1450mmx1200mm | 1650mmx1600mm |
| Min. Sheet Size | 500mmx440mm | 500mmx440mm | 500mmx440mm |
| Thickness of face Paper | 200~800g/㎡ | 200~800g/㎡ | 200~800g/㎡ |
| Thickness of Bottom Paper | 0-9mm | 0-9mm | 0-9mm |
| Max. Speed | 11000pcs/hr | 11000pcs/ hr | 11000pcs/ hr |
| Laminating Precision | ±1.5m/m | ±1.5m/m | ±1.5m/m |
| Total Weight | 6000kg | 6250kg | 6500kg |
| Total Length | 10700 mm | 10800 mm | 10900 mm |
| Operation Space (mm) | 3000x13500 | 3100x13500 | 3200x13500 |
| Power | 380V 3~(15hp） | 380V 3~(15hp） | 380V 3~(15hp） |

- Features of the machine:

  - General Introduction:

The QTM series High Speed Automatic Flute Laminator is suitable for the lamination of printed cardboard paper with 2 ply or 4 ply corrugated sheet which is mainly used in food, beverage boxes etc.

The machine adopts chasing registration method with the help of imported low-voltage parts, liquid sensor and movement control system.

  - Machine Structure:

Upper Feeding Part：Feed the paper of 200-800gsm.

Bottom Feeding Part：Feed different kinds of corrugated sheet between 0-9mm.

Conveyor：Press the laminated paper and convey to the paper delivery unit.

Gluing Part：Coating glue of the bottom paper.

  - Features by Parts:

    - Upper Feeding Part:

      - High speed feeder with 4 sucking suckers and 4 delivery suckers with the highest speed 16000 sheets per hour, which can easily match to the  lamination unit of the machine which the maximum speed is 11.000 sheets per hour.

# Double sucking rubber and single rubber forwarding which can avoid effectively double paper.

# Equipped with two blower to ensure paper separation smoothly.

# There are two side blowers as well. The position of the side blower can be adjusted to ensure the smooth feeding of paper.

# Top Paper Conveying Part:

# The conveying of the face paper unit adopts scale feeding method，Compared with paper to paper conveying，the advantage is that the conveying speed of face paper can be reduced，ensuring the smooth feeding of the paper when running in high speed, without worrying of the scraping of the paper by side lays and when the paper is uneven, the paper front will press the paper back to make the ahead paper even.

# Paper Pile Part:

# There is sub-paper feeding device there which can hold the paper pile when it is to be finished, so that the paper can be replied without stopping the machine

# Lay of the Paper Pile

# There also has paper pile lay at paper piling part which makes the paper piling easily. It is equipped with rough adjusting wheel and fine adjustment bar.

# Bottom Sheet Lay Adjustment: There is digital hand bar to adjust the bottom paper side lay which makes the operator to fix the bottom sheet lay easily by viewing the digital numbers.

# Puller For Top Paper at Top Paper Conveying Part:

# Side Lay Adjustment Wheel:  After starting the lamination, if fine adjustment at sides part needs to be adjusted, you can turn this wheel. Each circle can move the top paper 1.75 mm either at left or right direction.

# Order Change Operation: When order is changed, the operator can do the order change easily by turning these wheels which makes the operation easy and fast.

# The machine adopts imported liquid level controller for glue supply. When detecting no glue in the glue barrel, it can stop the feeder automatically to avoid waste of paper.

# Paper Detecting Pin: If the paper laminated does not goes smoothly to the conveyer, the detector will send signs to stop the machine.

# Water Damping Roller: It can not only wash the dirt out of the bottom paper back, but also can pasting water on the bottom paper to make it soft and even to facilitate the lamination.

# Special Designed Gluing System:  This anilox type gluing system will use 25-30 gsm of glue (according to the paper quality), which is a great saving in a year around production.

# Bearings: The bearings at key parts are NSK and non key parts are from good fame domestic producers.

# Taiwan EUROVAC vacuum pump

# Simens Main Motor

# Teeth Belt Driving System

# Plum key universal shaft for feeder which is more stronger and durable than hexagonal shaft.

# Taiwan CPG Speed reducer for top paper lifting pile.

# Man-machine interface which can display speed, malfunctions and adjustment

# Motion Control and Main Electric Cabinet:

# Switzerland Banmer photoelectric switch

# All the PLC input, output points can be displayed at any time on the screen

PLC Output and Input

# The special parameters on the touch screen can be adjusted according to the  paper type, for example, the distance of feeder lifting

# It is convenient when adjust the position of  face paper and bottom paper. If you want to the face paper exceed the bottom paper 3mm, enter 3 on the screen. The data can not be changed when the machine speed is changing, the max data can be 30-40.,it can satisfy the demand of some special user.

# Front-Lead Sun-Element Type Bottom Paper Feeding Unit:

# Installation Chart:

# Configurations:

| Name | Brand |
| --- | --- |
| PLC | SIMENS S7-200 |
| Servo motor and controller | JAPAN YASKAWA |
| The man-machine interface touch screen | TAIWAN WEINVEW |
| Frequency transformer | JAPAN MITSUBISHI E740 |
| Photoelectric switch | SWITZERLAND BANMER |
| Contactor | FRENCH SCHNEIDER |
| Relays | JANPAN OMRON |
| Button | SHANHAI TIANYI |
| Glue liquid control | JAPAN OMRAN |
| Cog belt | TAIWAN SANWU |
| The key bearing | JAPAN NSK |
| Other Bearings | RENBEN BEARING |
| Main Power Motor | GERMANY SIMENS |
| Air Pump | Tai Wan Brand EUROVAC Rotary Vane Pump |

# Attached Tools

| L type hexagonal Spammer | One set |
| --- | --- |
| T type hexagonal Spammer 5,6mm | Each of 1 branch |
| Monkey Wrench 12″ | 1PC |
| Plus Screwdriver | 1PC |
| Minus Screwdriver 150 | 1PC |
| Plum wrench openings | 10,12,13,14,17,19 (each1 PC) |
| Sharp-nose pliers 6″ | 1PC |
| Slip joint pliers 8″ | 1PC |
| Shaft retaining ring clip S | 1PC |
| Hole clasp clip R | 1PC |
| TOP Tape measure 3.6M | 1PC |
| Aluminum Ladder | 1PC |
| Tools Box | 1PC |
| Operation Manual | 1PC |
| Glue Barrel | 1PC |

# Attached Spare Parts:

| Tooth Belt 1728-D8M-30 | One Piece |
| --- | --- |
| Tooth Belt 856-D8M-20 | One Piece |
| Sucker Rubber Ring | 20PC |
| Paper Delivery plate | 1PC |
| Pre-piling paper trolley | 1PC |
| Wedge for paper pile | 4PC |
| Pallet (Wide) | 2PC |
| Pallet( narrow) | 4PC |

| Switzerland BANMER photoelectric switch | 1 PC |
| --- | --- |
| Tai Wan Yangming proximity switch | 1PC |
| 08B Chain Clip | 3PC |
| 10A Chain Clip | 3PC |
| 08B chain transition section | 3PC |
| 10A chain transition section | 3PC |

# Consumable Parts List

| Tooth Belts | The whole machine |
| --- | --- |
| Face paper conveying belt 2mm Nylon | The whole machine |
| All kinds of button switch | The whole machine |
| Copper block sheet | The whole machine |
| Feeder sucker | The whole machine |
| Feeder brush | The whole machine |

# Other information:

- The enclosed pictures are just for reference, kindly please make the specification and object as the standard.

- As for the overseas installation, the customer shall pay each installation person 50.00USD per day and bear the costs of air trip tickets, food and accommodation.

- The fabrication period is within 120 days and the installation period within around 15 days after the advance payment received.

- 30% advance payment paid by T/T before fabrication and 70% balance payment paid by	LC or TT  before delivery.

# Text boxes

Pressure Paper delivery

Front  lay  Laminating

Bottom feeding

Upper feeding

Side Blowing

SCALE FEEDING

Main Feeding Pallet

Sub Feeding Pallet

Fine Adjustment Bar

Rough Adjustment Wheel

Bottom Sheet Adjustment Digital Bar

Puller For Top Paper

Hand wheel

Paper thickness hand wheel

Glue Adjustment

Direction Sign

Digital Display

Automatic glue Supply  system

Paper Detection Switch

Water Damping Roller

Gluing Roller

Rubber Roller

Screw fastening logo

Imported Bearings

TaiWan CPG Reducer

Main Paper Feeding

Sub Paper Feeding

German siemensS7-200 series PLC

Yaskawa servo drive

French schneider contactor

Japan Mitsubishi E740

Frequency transformer

Switzerland Banmer photoelectric switch